## Slide 1: Dealing with Non Uninform Memory Access
Claude TADONKI
MINES ParisTech – PSL Research University
Paris - France
Universidade Federal Fluminense (Niteroi - Brasil) – May 15, 2019

## Slide 2: Major Concerns with Manycores
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
Concurrent accesses to main memory
More complicated cache hierarchy & coherence
Threads scheduling (static and dynamic)
Energy & cooling
Fault tolerance
Manycores can be used as
servers or as parallel computing machines

## Slide 3: NUMA: Concept & Packaging
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
UMA
Yinan Li et al.

## Slide 4: INTEL BROADWELL
Intel® Xeon® Processor E5-2699 v4
Released in April 2016
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
Each chip has 22 cores organized a 2 NUMA nodes
Each NUMA node has 11 cores
The processor has 2 chips, thus 2 x 2 = 4 NUMA nodes
The total number of cores is 11 x 4 = 44

## Slide 5: Why NUMA
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
SMP has a certain level of serialization of concomitant memory accesses
This serialization increases with the number of cores
CPU operates considerably faster than memory accesses: memory wall !!!
Applications with an intensive memory access will show very poor speedups.
NUMA configurations are designed to alleviate the main memory contention

## Slide 6: Analogy with a Supermarket
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
We fill our shopping basket if parallel (clients are completely independent)
But we experience an unpleasant serialization at the checkout

## Slide 7: Getting the NUMA configuration
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
numactl is a utility which can be used to handle NUMA considerations
We can see that we have 4 NUMA nodes (0-3), each with 11 cores
The node distances matrix helps to identify the NUMA topology

## Slide 8: NUMA Unaware Case
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
Good scalability within one NUMA node !!!
Parallelization of Wilson-Dirac operator on a Broadwell-EP

## Slide 9: Summary of NUMA considerations
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
NUMA Nodes are connected with QPI links
“Local accesses” are of course faster that “remote accesses”
Links between NUMA nodes are potentially subject to heavy contention
It is important to know the topology of the processor (memory and CPU cores)
Memory allocations and thread binding to specific nodes can be controlled by the programmer
NUMA-unaware programs are likely to yield a noticeably poor scalability

## Slide 10: Programming & Managing NUMA
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
NUMA considerations can be handled within programs through libraries like libnuma
#include <numa.h> All command start with the prefix numa_
The library allow to
  allocate memory on a specific node
  ask to interleave an array on all NUMA nodes
  check on which node a given memory space is allocated
  identified on which NUMA node a given core (logical id) belongs to
Such libraries should be used with flexibility in order to avoid portability issues
An efficient explicit management of NUMA considerations can improve scalability

## Slide 11: Programming & Managing NUMA
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
We can get the total number of NUMA nodes with numa_max_node() + 1
We can get the total number of cores with sysconf(_SC_NPROCESSORS_ONLN)
We can check if the system supports NUMA API with numa_available()

## Slide 12: Programming & Managing NUMA
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
We can get the total number of NUMA nodes with numa_max_node() + 1
We can get the total number of cores with sysconf(_SC_NPROCESSORS_ONLN)
We can check if the system supports NUMA API with numa_available()

## Slide 13: Programming & Managing NUMA
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
We can get the total number of NUMA nodes with numa_max_node() + 1
We can get the total number of cores with sysconf(_SC_NPROCESSORS_ONLN)
We can check if the system supports NUMA API with numa_available()
We allocate the memory on a specific node (node_id) using numa_malloc_onnode()
The memory allocated using numa_malloc_onnode() is released using numa_free()

## Slide 14: Programming & Managing NUMA
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
We can bind a thread to a specific core (using its id)
We should consider the global NUMA packaging when allocating a thread to a core

## Slide 15: NUMA-aware Wilson-Dirac
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
High Performance Computing and Simulation (HPCS) 2017 – Genoa (Italy)

## Slide 16: Harris Corner Detection
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019

## Slide 17: NUMA-aware Corner Detection
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019

## Slide 18: NUMA-aware Corner Detection
Non Uniform Memory Access (NUMA)
Claude TADONKI – UFF – Niteroi (Brazil) – May 15, 2019
Future Generation Computing Systems (FGCS) 2018

## Slide 19: End
Thanks for your attention
High Performance Computing
Claude TADONKI – UFRJ – Rio de Janeiro (Brazil) – May 13, 2019